oneOnAtATime

//LED Pin Variables
int ledPins[] = {2,3,4,5,6,7,8,9}; //An array to hold the pin each LED is connected to
        //i.e. LED #0 is connected to pin 2, LED #1, 3 and so on
        //to address an array use ledPins[0] this would equal 2
        //and ledPins[7] would equal 9

/*
 * setup() - this function runs once when you turn your Arduino on
 * We the three control pins to outputs
 */
void setup()
{

  //Set each pin connected to an LED to output mode (pulling high (on) or low (off)
  for(int i = 0; i < 8; i++){ //this is a loop and will repeat eight times
      pinMode(ledPins[i],OUTPUT); //we use this to set each LED pin to output
  } //the code this replaces is below

  /* (commented code will not run)
   * these are the lines replaced by the for loop above they do exactly the
   * same thing the one above just uses less typing
  pinMode(ledPins[0],OUTPUT);
  pinMode(ledPins[1],OUTPUT);
  pinMode(ledPins[2],OUTPUT);
  pinMode(ledPins[3],OUTPUT);
  pinMode(ledPins[4],OUTPUT);
  pinMode(ledPins[5],OUTPUT);
  pinMode(ledPins[6],OUTPUT);
  pinMode(ledPins[7],OUTPUT);
  (end of commented code)*/
}

/*
 * loop() - this function will start after setup finishes and then repeat
 * we call a function called oneAfterAnother(). if you would like a different behaviour
 * uncomment (delete the two slashes) one of the other lines
 */
void loop() // run over and over again
{
oneOnAtATime(); //this will turn one LED on then turn the next one
        //on turning the
        //former off (one LED will look like it is	scrolling
}

/*
 * oneOnAtATime() - Will light one LED then the next turning off all the others
 */
void oneOnAtATime(){
  int delayTime = 100; //the time (in milliseconds) to pause between LEDs
        //make smaller for quicker switching and larger for slower

  for(int i = 0; i <= 7; i++){
    int offLED = i - 1; //Calculate which LED was turned on last time through
    if(i == 0) { //for i = 1 to 7 this is i minus 1 (i.e. if i = 2 we will
      offLED = 7; //turn on LED 2 and off LED 1)
    } //however if i = 0 we don't want to turn of led -1 (doesn't exist)
        //instead we turn off LED 7, (looping around)
    digitalWrite(ledPins[i], HIGH); //turn on LED #i
    digitalWrite(ledPins[offLED], LOW); //turn off the LED we turned on last time
    delay(delayTime);
  }
}